|  | INTERNATIONAL PTY LTD |  |  |  |
| --- | --- | --- | --- | --- |
|  |  | Phone (03) 6264 1727 |  |
| PO Box 383 Huonville. Tas. 7109 | Fax (03) 6264 2297 |  |
| 2800 Huon Highway Huonville. Tas. 7109 | Mobile: 0417 503 064 |  |
|  |  | email: john@rowfit.com |
|  | RIGGER SHEET MEASURING INFORMATION |  |  |  |
| Tools Required | Straight Edge, Tape Measure or steel rule, protractor, parallel block |  |  |  |
| Dimension 'A' | This dimension is the MAXIMUM width of the boat at the point where the rigger bolts on |  |
| Dimension "B" | This is the distance from the top of the gunwale to the centre of the top bolt |  |  |
| Dimension "C" | This is the centre distance between the rigger bolts |  |  |  |
| Dimension "D" | This is the distance from the centre of the bottom bolt to the point where the side board angle changes |
| Dimension "E" | This is the horizontal dimension between the centre line of the shoulders E1 & E2 may not be the same |
| Dimension "F" | This is the angle of the side board as shown |  |  |  |
| Dimension "G" | For Sculling riggers this is your mid range span between centre of pins |  |  |
|  | For Rowing Riggers this is your mid range span from centre line of boat to centre of pin |  |
|  | (Length of slot in heads = 50mm) |  |  |  |
| Dimension "H" | This is the distance from the gunwale to top of seat |  |  |  |
| Dimension "I" | This is the thickness of the lip of the gunwale |  |  |  |
| Dimension "J" | This dimension will put your head to the stern or the bow of the boat. If you want your head square |
|  | off the shoulder write 0mm |  |  |  |